## Slide 1
By:
Shivam Raj | Desari Yogesh Lesyak | Armaan Anil Narang | Anushka GuptaShivam Raj | Desari Yogesh Lesyak | Armaan Anil Narang | Anushka Gupta
1DS25EC244 | 1DS25EC082 | 1DS25EC050 | 1DS25EC047
Under the Guidance of :
Dr. Sumit Swain
Assistant Professor, Dept. of ECE, DSCE
DAYANANDA SAGAR COLLEGE OF ENGINEERING
(An Autonomous Institute affiliated to VTU)
Department Of Information Science And Engineering
INNOVATION AND DESIGN THINKING LAB (1BIDTL158) INNOVATION AND DESIGN THINKING LAB (1BIDTL158) INNOVATION AND DESIGN THINKING LAB (1BIDTL158) INNOVATION AND DESIGN THINKING LAB (1BIDTL158) INNOVATION AND DESIGN THINKING LAB (1BIDTL158) INNOVATION AND DESIGN THINKING LAB (1BIDTL158)
First Year Mini Project progress Presentation on
Nanoparticles based Sensors for Microplastics Detection in Drinking Water based on Fractional Order Modelling
Notes: Speaker Note:

## Slide 2: Agenda
1. Introduction
2. Literature Survey
3. Problem Identification
4. Methodology & Proposed System
5. Sensor Fabrication & Hardware Design
6. Initial Data Collection & Results
7. Current Status (50% Completed)
8. Future Work & Remaining Milestones
9. References

## Slide 3
1. Introduction
* Microplastic contamination in drinking water is a growing global health and environmental concern.
* Microplastics (< 5 mm) originate from plastic waste breakdown, industrial discharge, and daily human activities.
* Conventional detection methods (filtration, microscopy, spectroscopy) are costly and require lab facilities.
* This project develops a simple, low-cost capacitive sensor using MWCNT-epoxy nanocomposite dielectric.
* The sensor detects microplastics by measuring changes in impedance and fractional-order parameter.
* Fractional-order electrical modelling accurately captures the non-ideal behaviour of the sensor.
* The approach is non-destructive, reagent-free, and suitable for routine water quality monitoring.

## Slide 4
2. Literature Survey
* Filtration-Microscopy: common but slow, expert-intensive, unsuitable for on-site testing.
* Spectroscopic methods (FTIR, Raman): accurate but require complex instrumentation.
* Capacitive/impedance sensors: detect changes in liquid electrical properties — simpler and faster.
* CNT/polymer nanocomposites enhance sensitivity via improved charge transport and interfacial interactions.
* Fractional-order CPE models effectively represent non-ideal, memory-dependent sensor behaviour.
Gap Identified:
* No prior work combines CNT-epoxy capacitive sensors with fractional-order phase analysis for microplastic detection.
Key References: Swain et al. (IETE 2023), Swain et al. (AEU 2024), Nayak et al. (J. Food Eng. 2025).

## Slide 5
3. Problem Identification
Problem Statement:
Existing microplastic detection methods require expensive equipment and are unsuitable for routine on-site monitoring.
A simple, low-cost, non-destructive technique is needed for regular drinking water quality assessment.
Objectives:
1. Fabricate a capacitive sensor using MWCNT-epoxy composite as the sensing dielectric.
2. Study the effect of microplastics on output voltage amplitude and phase under AC excitation.
3. Analyse changes in electrical response caused by different microplastic concentrations.
4. Apply fractional-order model to describe non-ideal sensor behaviour.
5. Evaluate the sensor for drinking water quality monitoring applications.
SDG Alignment: SDG 6 (Clean Water & Sanitation) | SDG 14 (Life Below Water)

## Slide 6
4. Methodology & Proposed System
System Block Diagram:
[Function Generator: 1 kHz to 10 MHz] --> [CNT-Epoxy Capacitive Sensor in Water] --> [DSO]
Working Principle:
* AC voltage applied across sensor; DSO records output amplitude and phase at each frequency.
* Microplastics displace water between electrodes --> change in effective dielectric constant.
* Changes in impedance magnitude and phase shift indicate microplastic presence and concentration.
Fractional-Order Model (CPE): Z(jw) = 1 / [C * (jw)^a]
* C = capacitance (uF); a = fractional order exponent (0 < a < 1).
* Both C and a increase proportionally with microplastic concentration.
* Calibration equations derived: y = 0.0051x (linear) and y = 7.6*(e^(0.47*(c-17))-1) (exponential).

## Slide 7
5. Sensor Fabrication & Hardware Design
Sensing Material (Dielectric):
* 50 mg Multi-Walled Carbon Nanotubes (MWCNT) mixed with 10 g epoxy resin; cured.
* MWCNT enhances electrical response through improved charge transport pathways.
Sensor Structure:
* Two parallel copper plate electrodes with MWCNT-epoxy composite as dielectric.
* Housed in 3D-printed rectangular casing (designed using 3D printing software).
Experimental Setup (Assembled & Verified):
* Function Generator connected to sensor; DSO monitors input and output signals simultaneously.
* Channel 1 (DSO): input from generator | Channel 2 (DSO): output across sensor.
* Frequency swept from 1 kHz to 10 MHz; peak-to-peak voltage and phase recorded at each point.

## Slide 8
6. Initial Data Collection & Results
Samples Tested So Far: 0 mg, 10 mg, 20 mg microplastics per 250 ml water.
Observations:
* Clean water: voltage decreases gradually with frequency (characteristic capacitive response).
* With microplastics: voltage decreases more rapidly; phase shift increases with concentration.
* Distinct separation between curves confirms sensor sensitivity to microplastic content.
Extracted Electrical Parameters (Partial Dataset):
Concentration Capacitance Phase (6-500 kHz) Fractional Order (a)
0 mg / 250 ml 13.5 uF -7.5 deg 0.083
10 mg / 250 ml 16.8 uF -10.5 deg 0.116
20 mg / 250 ml 17.9 uF -15.0 deg 0.167
Note: Data for 30 mg/250 ml to be completed in upcoming weeks.

## Slide 9
7. Current Status (50% Completed)
Phase 1: Problem Identification & Literature Survey -- COMPLETED (Weeks 1-4)
-> Team formed; topic finalized; 6+ papers reviewed; SDG alignment identified.
Phase 2: Concept Development & Design -- COMPLETED (Weeks 5-7)
-> CNT-epoxy composite design finalized; 3D sensor casing designed & printed; materials procured.
Phase 3: Prototype Development -- COMPLETED (Weeks 8-11)
-> Sensor fabricated & assembled; experimental circuit set up and verified.
-> Baseline (clean water) measurements done; initial microplastic experiments conducted.
-> Partial data collected for 0 mg, 10 mg, 20 mg concentrations.
Overall Progress: |XXXXXXXXXX...........| ~50% Complete
CIE Phases 1-3 completed: 10 + 20 + 30 = 60% of CIE weightage covered.

## Slide 10
8. Future Work & Remaining Milestones
Phase 4: Testing & Validation (Weeks 12-13)
-> Collect data for 30 mg/250 ml; conduct repeated measurements for statistical validation.
-> Verify calibration equations with unknown water samples.
Phase 5: Documentation & Analysis (Weeks 13-14)
-> Complete project report with full data analysis, error analysis, and comparison tables.
-> Finalise all graphs: Magnitude vs Frequency, Phase vs Frequency, Conc. vs a, Conc. vs C.
Phase 6: Final Demo & Social Pitch (Weeks 15-16)
-> Develop optimisation algorithm to estimate microplastic concentration from sensor readings.
-> Build software interface for real-time microplastic content display.
-> Final project demonstration and IPBL social pitch presentation.

## Slide 11
9. References
[1] S. Swain, M. C. Tripathy, and S. Behera, 'Particle swarm optimization-based bandpass filter using switched-fractional capacitors,' IETE J. Res., vol. 69, no. 12, pp. 9183-9194, 2023.
[2] S. Swain, M. C. Tripathy, et al., 'Implementation of a fractional-inductor and its performance in a high-frequency LalphaR integrator circuit,' AEU, p. 155114, 2024.
[3] S. Swain, M. C. Tripathy, S. Behera, and A. Dastidar, 'Experimental analysis of ripening stages using fractional-order bio-impedance modelling,' IETE J. Res., 2025.
[4] B. Nayak, S. Swain, and M. C. Tripathy, 'Fractional order bioimpedance modeling for sensing fruit properties,' J. Food Eng., vol. 397, 2025.
[5] S. Swain, M. C. Tripathy, K. C. Bhuyan, and S. Behera, 'Wide-band fractional-order filter design using coaxial TEM fractional-inductor,' Next Research, 2025.
[6] B. Nayak, S. Swain, H. Patra, and M. C. Tripathy, 'Fractional capacitor-based bio-impedance analysis for sensing pH in potatoes,' ICDCECE, 2025.

## Slide 12: Thank You